PRODUCT FEATURES

DESCRIPTION

Steel access ladder, floor and wall mounted.

BASIC USES / RELATED USES

To access floor or roof through access doors or hatches.

PRODUCT ATTRIBUTES AND CHARACTERISTICS

Wall or floor mounted, using L-brackets turned inward or outward.

Rungs spaced at 305 mm (12 inch) centres.

PRODUCT PROPERTIES

MATERIALS

Steel:  Hot-rolled (hot-dipped galvanized is optional).

Rungs:  Round, 19 mm (3/4 inch) diameter, with raised surface for added foot grip.

Risers:  Flat bars, 9.5 x 64 mm (3/8 x 2-1/2 inch).

Brackets:  Flat bars, 9.5 x 64 mm (3/8 x 2-1/2 inch), with pre-drilled 16 mm (5/8 inch) diameter mounting holes.

DIMENSIONS

Rungs 406 mm (16 inches) wide, spaced 305 mm (12 inch) on centre.

Risers:  Length (ladder height) to suit project.

Brackets: 216 x 64 mm (8-1/2 x 2-1/2 inch); suitable to position ladder 152 mm (6 inches) from wall surface.

SHOP FABRICATION AND ASSEMBLY

Connections are welded.

Brackets may be turned inward (toward rungs) or outward (away from rungs).

FINISH

Grey oxide primer.

Optional:  Hot-dipped galvanized.

PRODUCT PLACEMENT

INSTALLATION

Coordinate with matching roof hatch or floor access door.

| Corporate Identification |
| --- |
|  | Maxam Metal Products Limited |
|  | Unit 5 – 7978 North Fraser Way, Burnaby, B.C. Canada V5J 0C7 |
|  | Toll Free Phone: 866-446-2926 Toll Free Fax: 866-436-2926 Direct Phone: 604-433-4243 Direct Fax: 604-433-4148 E-mail: info@maxammetal.com Internet: www.maxammetal.com |
| Classification and Filing |
|  | MasterFormat 2004: |
|  |  | Section 07 72 33 – Roof Hatches |
|  |  | Section 08 31 14 - Floor Access Doors |
|  |  | Section 05 51 33 - Metal Ladders |
|  | MasterFormat 1995: |
|  |  | Section 07720 – Roof Hatches |
|  |  | Section 08311 - Floor Access Doors |
|  |  | Section 05510 - Metal Ladders |

END