PRODUCT FEATURES

DESCRIPTION

Safety grab handle, for mounting on roof hatches.

BASIC USES

To assist the safe entry and exit from roof hatches.

PRODUCT ATTRIBUTES AND CHARACTERISTICS

Does not obstruct hatch opening.

One piece, heavy duty steel construction, safety red colour.

SELECTION CRITERIA

Universal mounting on right or left side of hatch.

Can be added to existing installed roof hatches.

PRODUCT PROPERTIES

COMPOSITION

Grab Handle:  Steel tubing, heavy gauge wall, 35 mm (1-3/8 inch) diameter.

Mounting Bracket:  Cold rolled steel, 2.75 mm (12 ga) thick.

Hardware:

Bolts:  3/8 x 2-1/4 inch size, plated.

Lock Nuts:  Nylon, 3/8 inch size.

SHAPE AND DIMENSIONS

Width:  L-shaped, 305 mm (12 inches) each side.

Height:  305 mm (12 inches).

FINISH, COLORS

Powder coated, safety red colour.

PRODUCT PLACEMENT

INSTALLATION

Coordinate with matching roof hatch.

| Corporate Identification |
| --- |
|  | Maxam Metal Products Limited |
|  | Unit 5 – 7978 North Fraser Way, Burnaby, B.C. Canada V5J 0C7 |
|  | Toll Free Phone: 866-446-2926 Toll Free Fax: 866-436-2926 Direct Phone: 604-433-4243 Direct Fax: 604-433-4148 E-mail: info@maxammetal.com Internet: www.maxammetal.com |
| Classification and Filing |
|  | MasterFormat 2004: |
|  |  | Section 07 72 33 – Roof Hatches |
|  | MasterFormat 1995: |
|  |  | Section 07724 – Roof Hatches |

END